## Slide 1: MSOrganiser Summary
  Input MRM data
Updated: 2021-05
  Input Annotation File
  Transition Name Annotation
Refer to the summary sheet or user manual to see how it is used.
MRM transition names data form | Compulsory column names | Restricted column names
Agilent’s WideTable form | Data File (from Sample) | Quantitation Message (from Sample) Columns from Qualifier Methods ISTD Compound Methods ISTD Compound Results
Agilent’s CompoundTable form | Name (from Compound Method) Data File (from Sample) | Quantitation Message (from Sample) Columns from Qualifier Methods Qualifier Results ISTD Compound Methods ISTD Compound Results
  Example
  Organise MRM data to tidy form
  Table of valid MRM data formats
  Load MRM Files and specify MS_FileType and
  Output Directory
  2. Choose Output options
  3. Click start to organise data
When doing normalisation and concentration calculation, MS Template Creator Excel file must be provided
By default, organised data will be output into an Excel file in wide table form
A report pdf file will also be provided to record the parameters used
  Sample Annotation
  ISTD Annotation
  Additional Features
Different output format for the organised data.
Set Transpose_Results to True to let the sample name be the columns instead of the transition names.
Options to output results in a Long Table are available

## Slide 2: MSOrganiser Summary
  Additional Features
Updated: 2021-05
Select the following concatenation options to combine multiple input files to one result file.
If there is a need to calculate the normalised area and concentration, set Set Allow_Multiple_ISTD to True