## Slide 1: MSOrganiser Summary
  Input Raw data
Updated: 2021-10
  Input Annotation File
  Transition Name Annotation
Here are some input examples.
  Organise MRM data to tidy form
  Table of valid MRM data formats
  Load MRM Files and specify MS_FileType and
  Output Directory
  2. Choose Output options
  3. Click start to organise data
When doing normalisation and concentration calculation,
By default, organised data will be output into an Excel file in wide table form
A report pdf file will also be provided to record the parameters used
  Sample Annotation
  ISTD Annotation
MRM transition names data form | Compulsory column names |  | Restricted column names
 | Without Qualifiers | With Qualifiers | 
Agilent’s WideTable form | Sample Data File Compound Results Area | Qualifier Results Area | Sample Quantification Message Columns from ISTD Compound Methods ISTD Compound Results
Agilent’s CompoundTable form | Sample Data File Compound Method Name Compound Results Area | Qualifier Method Transition Qualifier Results Area | 
  Example
Agilent’s Wide Table form
Agilent’s Wide Table form with Qualifier
Agilent’s Compound Table form
Agilent’s Compound Table form with Qualifier
  Additional Features
Different output format for the organised data.
Set Transpose_Results to True to let the sample name be the columns instead of the transition names.
Select the following concatenation options to combine multiple input files to one result file.
Refer to the summary sheet or manual to see how it is used.
MS Template Creator Excel file must be provided.

## Slide 2: MSOrganiser Summary
  Additional Features
Updated: 2021-10
If there is a need to calculate the normalised area and concentration, set Allow_Multiple_ISTD to True
Options to output results in a Long Table are available

## Slide 3: Concentration calculation of non-liquid samples
Calculations explanation:
take the ISTD conc in nM (fmol/uL).
divide it by the ratio between volume of reconstituted extract before injection in uL and volume of added standard in uL (usually 200uL/10uL) to know the ISTD conc in sample.
multiply this value by the ratio of area endogenous/area ISTD to obtain conc of endogenous
multiply conc of endogenous by volume of reconstituted extract before injection in uL to give concentration of endogenous sample in fmol
divide by the unit of the sample (weight of the tissue) giving the concentration unit to be (fmol/unit of sample)

## Slide 4: Cell number concentration calculation

## Slide 5: Cell number concentration calculation

## Slide 6: Cell number concentration calculation
is
is
cell number
Assuming the analyte and the selected ISTD have identical response factors, the concentration of an analyte in the sample can be calculated as
where
cAnalyte: molar concentration of the analyte in the sample
AreaAnalyte: peak area of analyte,
AreaISTD: peak area of ISTD,
vISTD: extracted volume from the ISTD mixture,
Sample_Amount: quantity of the sample,
cISTD: concentration of the ISTD in the ISTD mixture
is
To put in MS Template Creator

## Slide 7: Protein concentration calculation
Protein homogenate volume
BuMe with ISTD volume

## Slide 8: Protein concentration calculation

## Slide 9: Protein concentration calculation
Assuming the analyte and the selected ISTD have identical response factors, the concentration of an analyte in the sample can be calculated as
where
cAnalyte: molar concentration of the analyte in the sample
AreaAnalyte: peak area of analyte,
AreaISTD: peak area of ISTD,
vISTD: extracted volume from the ISTD mixture,
Sample_Amount: quantity of the sample,
cISTD: concentration of the ISTD in the ISTD mixture
is
is

## Slide 10: To put in MS Template Creator
is
is
Protein concentration calculation